## Slide 1: Privacy and Security in RFID Based Systems
NC 812/ESD 812

## Slide 2: RFID System

## Slide 3: Reading Tags
The read process starts when an RFID reader sends out a query message
  Invites all tags within range to respond
  More than one RFID tag may respond at the same time
    This causes a collision
  Reader cannot accurately read information from more than one tag at a time
Reader must engage in a special singulation protocol to talk to each tag separately

## Slide 4: Privacy and Security Issues
The contents of an RFID tag can be read after the item leaves the supply chain:
An RFID tag cannot tell the difference between one reader and another.
RFID scanners are very portable; RFID tags can be read from a distance, from a few inches to a few yards.
This allows anyone to see the contents of your purse or pocket as you walk down the street.

## Slide 5: Privacy and Security Issues
RFID tags are difficult to remove:
RFID tags are difficult to for consumers to remove; some are very small (less than a half-millimeter square, and as thin as a sheet of paper).
Others may be hidden or embedded inside a product where consumers cannot see them.
New technologies allow RFID tags to be "printed" right on a product and may not be removable at all.

## Slide 6: Privacy and Security
RFID tags can be read without your knowledge.
Since the tags can be read without being swiped or obviously scanned (as is the case with magnetic strips or barcodes), anyone with an RFID tag reader can read the tags embedded in your clothes and other consumer products without your knowledge.

## Slide 7: Privacy and Security
RFID tags with unique serial numbers could be linked to an individual credit card number.
At present, the Universal Product Code (UPC) implemented with barcodes allows each product sold in a store to have a unique number that identifies that product.
When the item is scanned for purchase and is paid for, the RFID tag number for a particular item can be associated with a credit card number.

## Slide 8: Threats to RFID (STRIDE Model)
Spoofing identity. Spoofing occurs when an attacker successfully poses as an authorized user of a system.
Tampering with data. Data tampering occurs when an attacker modifies, adds, deletes, or reorders data.
Repudiation. Repudiation occurs when a user denies an action and no proof exists to prove that the action was performed.
Information disclosure. Information disclosure occurs when information is exposed to an unauthorized user.
Denial of service. Denial-of-service denies service to valid users. Denial-of-service attacks are easy to accomplish and difficult to guard against.
Elevation of privilege. Elevation of privilege occurs when an unprivileged user or attacker gains higher privileges in the system than what they are authorized.

## Slide 9: Spoofing: Example
A competitor or thief performs an unauthorized inventory of a store by scanning RFID EPC tags with an unauthorized reader to determine the types and quantities of items.
An unauthorized reader can query the tag for the EPC number because most tags used in the supply chain respond to any reader.

## Slide 10: Tampering with Data
Data tampering occurs when an attacker modifies, adds, deletes, or reorders data.
An attacker modifies a tag.
  An attacker modifies the tag in a passport to contain the serial number associated with a terrorist or criminal or vice versa.
  An attacker modifies the EPC number on tags in the supply chain, warehouse, or store disrupting business operations and causing a loss of revenue.
  An attacker modifies a high-priced item’s EPC number to be the EPC number of a lower cost item.

## Slide 11: Data Tampering
An attacker deletes data on a tag.
  An attacker kills tags in the supply chain, warehouse, or store disrupting business operations and causing a loss of revenue. EPCglobal proposed that a tag have a “kill” command to destroy it to protect consumer privacy. If implemented in the tag, an attacker can “kill” the tag if the password is known. Class-0, Class-1 Gen-1, and Class-1 Gen-2 tags have kill commands.

## Slide 12: Repudiation
Repudiation threats occur when a user denies an action and no proof exists to prove that the action was performed.
  A retailer denies receiving a certain pallet, case, or item. A non-repudiation protocol is required to ensure that neither the sender nor the receiver can deny actions.

## Slide 13: Information Disclosure
Information disclosure occurs when information is exposed to an unauthorized user. It is a threat to privacy if it is information about an individual.
  An attacker blackmails an individual for having certain merchandise in their possession.
  A fixed reader at a retail counter identifies the tags of a person and shows the similar products on the nearby screen to a person to provide individualized marketing.
  A mugger marks a potential victim by querying the tags in possession of an individual to determine if they are carrying valuable or wanted items.

## Slide 14: Denial of Service
Denial-of-service denies service to valid users. Denial-of-service attacks are easy to accomplish and difficult to guard against.
  An attacker kills tags in the supply chain, warehouse, or store disrupting business operations and causing a loss of revenue
  A shoplifter carries a blocker tag that disrupts reader communication to conceal the stolen item .

## Slide 15: Blocker Tag
A blocker tag is a RFID tag that responds positively to all unauthorized requests, thus blocking some scanners from reading any RFID tags placed nearby. The tags are designed to protect privacy.
  It simulates many ordinary RFID tags simultaneously and renders specific zones to be private or public. The blocker tag could simulate all RFID tags or it could simulate portions of the EPC address space.

## Slide 16: Some Solutions
The Faraday Cage approach: An RFID tag may be shielded from scrutiny using what is known as a Faraday Cage— a container made of metal mesh or foil that is impenetrable by radio signals (of certain frequencies). Been used by thieves in retail shops to circumvent shoplifting-detection mechanisms.

## Slide 17: Some Solutions
The Active Jamming Approach: Active jamming of RF signals is another, related physical means of shielding tags from view. The consumer could carry a device that actively broadcasts radio signals so as to block and/or disrupt the operation of any nearby RFID readers.