## Slide 1: Probabilistic Data Fusion
NC 812/ESD 812

## Slide 2: Introduction
Uncertainty lies at the heart of all descriptions of the sensing and data fusion process. An explicit measure of this uncertainty must be provided to enable sensory information to be fused in an efficient and predictable manner.
Probabilistic models provide a powerful and consistent means of describing uncertainty in a broad range of situations and leads naturally into ideas of information fusion and decision making. Probability is the only rational way to model uncertainty (in my opinion).
Probabilistic models sometimes cannot capture all the information that we need to define and describe the operation of a sensing and data fusion system. For example it would be difficult to imagine using probabilistic models alone to capture the uncertainty and error introduced by the dependence of an active electro-magnetic sensor information on beam-width and radiation frequency effects

## Slide 3: Fusion Rules
Hard decision Combining
OR, AND, Majority Logic
Soft decision Combining
Log-Likelihood Ratio Test

## Slide 4: Fusion
Due to its implementation simplicity 𝑘- out-of-𝑁 fusion rule is common for combining the local binary decisions.
In this case, the central entity will decide that the event of interest has occurred when 𝑘 or more received local decisions are in support.
When 𝑘 = 1, the fusion rule becomes an OR-fusion rule and if 𝑘 = 𝑁, it becomes an AND rule.

## Slide 5: Fusion
Let 𝐷𝑖 to be the local binary sensing decision of the 𝑖th sensor,
  𝐷𝑖 = 0 for 𝐻0 and
  𝐷𝑖 = 1 for 𝐻1
Thus the resulting 𝑘-out-of-𝑁 binary hypothesis testing problem is given by
By choosing a common threshold, 𝜆 for each sensor, the global probabilities of detection 𝑄𝑑 and false alarm 𝑄𝑓 can be obtained

## Slide 6: Qd and Qf
The global probability of detection and false alarm can be computed as,

## Slide 7: Example
Consider a system where Pd is 0.9 and Pf = 0.1. If decisions from 9 sensors are available, the resulting Qd and Qf for different fusion schemes is given by,
OR Fusion, k=1,
  Qd ~1
  Qf = 0.6126
AND Fusion, k=9
  Qd=0.3874, Qf~0
Majority Logic, k=5
  Qd=0.9991
  Qf=0.00089

## Slide 8: Probabilistic Fusion
Probabilistic data fusion methods are generally based on Bayes’ rule for combining prior and observation information. Practically, this may be implemented in a number of ways: through the use of the Kalman and extended Kalman filters and so on.
Bayes’ rule lies at the heart of most data fusion methods. In general, Bayes’ rule provides a means to make inferences about an object or environment of interest described by a state x, given an observation z.

## Slide 9: Bayes’ Rule
Bayes’ rule requires that the relationship between x and z be encoded as a joint probability or joint probability distribution P(x, z) for discrete and continuous variables respectively.
The chain-rule of conditional probabilities can be used to expand a joint probability in two ways
P(x, z) = P(x|z)P(z) = P(z|x)P(x)
Rearranging in terms of one of the conditionals, Bayes’ rule is obtained
P(x|z) = P(z|x)P(x)/P(z)

## Slide 10: Bayes’ Rule
The value of this result lies in the interpretation of the probabilities P(x|z), P(z|x), and P(x). Suppose it is necessary to determine the various likelihoods of different values of an unknown state x.
There may be prior beliefs about what values of x might be expected, encoded in the form of relative likelihoods in the prior probability P(x).
To obtain more information about the state x an observation z is made. These observations are modelled in the form of a conditional probability P(z|x) which describes, for each fixed state x, the probability that the observation z will be made; i. e., the probability of z given x.
The new likelihoods associated with the state x are computed from the product of the original prior information and the information gained by observation.

## Slide 11: Posterior Probability
This is encoded in the posterior probability P(x|z) which describes the likelihoods associated with x given the observation z. In this fusion process, the marginal probability P(z) simply serves to normalize the posterior and is not generally computed.
The marginal P(z) plays an important role in model validation or data association as it provides a measure of how well the observation is predicted by the prior.
The value of Bayes’ rule is that it provides a principled means of combining observed information with prior beliefs about the state of the world.

## Slide 12: Example
Consider a case where there are 3 types of hypotheses,
X0: No fire
X1: May be fire
X2: Definitely fire
Single sensor observes the event and returns reading z in three ranges.
z0: No fire
z1: May be fire
z2: Definitely fire

## Slide 13: Likelihood Matrix
The sensor model is described by the likelihood matrix P (z|X):
Likelihood matrix is a function of both z and X.
For a fixed state, it describes the probability of a particular observation being made (the rows of the matrix).
For an observation it describes a probability distribution over the values of true state (the columns) and is then the Likelihood Function.
 | z0 | z1 | z2
X0 | 0.7 | 0.2 | 0.1
X1 | 0.2 | 0.6 | 0.2
X2 | 0.1 | 0.2 | 0.7

## Slide 14: Sensor Model
The conditional probability P(z, x) serves the role of a sensor model and can be thought of in two ways. First, in building a sensor model, the probability is constructed by fixing the value of x = x and then asking what probability density P(z|x = x) on z results.
Conversely, when this sensor model is used and observations are made, z = z is fixed and a likelihood function P(z = z|x) on x is inferred. The likelihood function, while not strictly a probability density, models the relative likelihood that different values of x gave rise to the observed value of z.
The product of this likelihood with the prior, both defined on x, gives the posterior or observation update P(x|z). In a practical implementation, P(z|x) is constructed as a function of both variables (or a matrix in discrete form). For each fixed value of x, a probability density on z is defined. Therefore as x varies, a family of likelihoods on z is created.

## Slide 15: Multi-sensor Fusion
The multi-sensor form of Bayes’ rule requires conditional independence
where C is a normalising constant. Equation above is known as the independent likelihood pool. This states that the posterior probability on x given all observations Zn, is simply proportional to the product of prior probability and individual likelihoods from each information source.

## Slide 16: Recursive Bayes Rule
The recursive form of Bayes rule is as,
we need compute and store only posterior density P(x|Z k−1) which contains a complete summary of all past information. When the next piece of information P(zk|x) arrives, the previous posterior takes on the role of the current prior and the product of the two becomes, when normalised, the new posterior.

## Slide 17: Bayesian Filtering
Filtering is concerned with the sequential process of maintaining a probabilistic model for a state which evolves over time and is periodically observed by a sensor. Filtering forms the basis for many problems in tracking and navigation.
The general filtering problem can be formulated in Bayesian form. This is significant because it provides a common representation for a range of discrete and continuous data fusion problems without recourse to specific models.
Define xt as the value of a state of interest at time t. This may, describe a feature to be tracked, the state of a process being monitored, or the location of a platform for which navigation data is required. For convenience, and without loss of generality, time is defined at discrete times tk=k.

## Slide 18: Bayesian Filtering
At a time instant k, the following quantities are defined:
  xk: The state vector to be estimated at time k,
  uk: A control vector, assumed known, and applied at time k−1 to drive the state from xk−1 to xk at time k,
  zk: An observation taken of the state xk at time k.
In addition, the following sets are also defined.
The history of states:
  Xk = {x0, x1, ・ ・ ・ , xk} = {Xk−1, xk}.
The history of control inputs:
  Uk = {u1, u2, ・ ・ ・ , uk} = {Uk−1, uk}.
The history of state observations:
  Zk = {z1, z2, ・ ・ ・ , zk} = {Zk−1, zk}.

## Slide 19: Bayesian Filtering
In probabilistic form, the general data fusion problem is to find the posterior density
P(xk | Zk,Uk,x0)
for all times k given the recorded observations and control inputs up to and including time k together with knowledge of the initial state x0.
Bayes’ rule can be used to write above equation in terms of a sensor model P(zk|xk) and a predicted probability density P(xk | Zk−1,Uk, x0) based on observations up to time k−1 as

## Slide 20: Example
Consider a case where there are 3 types of hypotheses,
X0: Target 1
X1: Target 2
X2: No target
Single sensor observes the event and returns reading z in three ranges.
z0: Target 1
z1: Target 2
z2: No target

## Slide 21: Likelihood Matrix
The sensor model is described by the likelihood matrix P (z|X):
Likelihood matrix is a function of both z and X.
For a fixed state, it describes the probability of a particular observation being made (the rows of the matrix).
For an observation it describes a probability distribution over the values of true state (the columns) and is then the Likelihood Function.
 | z0 | z1 | z2
X0 | 0.45 | 0.45 | 0.1
X1 | 0.45 | 0.45 | 0.1
X2 | 0.1 | 0.1 | 0.8

## Slide 22: Example
The posterior distribution of the true state x after making an observation z = zi is given by
P(x|zi) = αP(zi| x)P(x)
α is a normalizing constant so that sum, over x, of posteriors is 1.
Assume a non-informative prior: P(x) = (0.333, 0.333, 0.333)
Observe z = z0, then posterior is P(x|z0) = (0.45, 0.45, 0.1)
The first column of the likelihood matrix above; the likelihood function given z1 has been observed. This posterior becomes the new prior and if we observe z = z1 again, then
P(x|z0) = αP(z0|x)P(x)
= α × (0.45, 0.45, 0.1) ⊗ (0.45, 0.45, 0.1)
= (0.488, 0.488, 0.024)

## Slide 23: Data Fusion using Bayes Theorem
Consider the set of observations
Zn = {z1 ∈ Z1, ・ ・ ・ , zn ∈ Zn} .
Posterior distribution given observation set is naively
P(x|Zn) = P(Zn|x)P(x)/P(Zn)
= P(z1, ・ ・ ・ , zn |x)P(x)/P(z1, ・ ・ ・ , zn)
The joint distribution P(z1, ・ ・ ・ , zn | x) must be known completely
Assume conditional independence,
P(z1, ・ ・ ・ , zn | x) = P(z1 | x) ・ ・ ・ P(zn | x)

## Slide 24: Independence Likelihood Pool

## Slide 25: Data Fusion using Bayes Theorem
The effectiveness of fusion relies on the assumption that the information obtained from different information sources is independent when conditioned on the true underlying state of the world.
P(z1, ・ ・ ・ , zn) = P(z1) ・ ・ ・ P(zn),
As each piece of information depends on a common underlying state x ∈ X.
Conversely, it is generally quite reasonable to assume that the underlying state is the only thing in common between information sources and so once the state has been specified it is correspondingly reasonable to assume that the information gathered is conditionally independent given this state.

## Slide 26: Example
Consider a case where there are 3 types of hypotheses,
X0: Target 1
X1: Target 2
X2: No target
Single sensor observes the event and returns reading z in three ranges.
z0: Target 1
z1: Target 2
z2: No target

## Slide 27: Example
Consider a second sensor which makes the same three observations as the first sensor, but whose likelihood matrix P2(z2|x) is described by
Whereas the first sensor was good at detecting hypothesis 1 and 2, but not at distinguishing between different target types, this second sensor has poor overall detection probabilities but good target discrimination capabilities.
With a uniform prior, observe z = z0 then the posterior is (the first column of the likelihood matrix)
P(x|z0) = (0.45, 0.1, 0.45)
 | z0 | z1 | z2
X0 | 0.45 | 0.1 | 0.45
X1 | 0.1 | 0.45 | 0.45
X2 | 0.45 | 0.45 | 0.1

## Slide 28: Example
It makes sense to combine the information from both sensors to provide both good detection and good discrimination capabilities.
Overall likelihood function for the combined system is
P12(z1, z2| x) = P1(z1|x)P2(z2|x)
Observe z1 = z0 and z2 = z0 and assuming a uniform prior probability, then posterior is
P(x|z0,z0) = αP12(z0,z0|x)
= αP1(z0|x)P2(z0|x)
= α × (0.45, 0.45, 0.1) ⊗ (0.45, 0.1, 0.45)
= (0.6924, 0.1538, 0.1538)
Sensor 2 adds substantial target discrimination power at the cost of a slight loss of detection performance for the same number of observations.

## Slide 29: Data Fusion Using Bayes Rule
Repeating this calculation for each z1, z2 observation pair:
z1 = z0 (observation from first sensor is z1)
z2 | z0 | z1 | z2
x1 | 0.6924 | 0.1538 | 0.488
x2 | 0.1538 | 0.6924 | 0.488
x3 | 0.1538 | 0.1538 | 0.024

## Slide 30: Data Fusion
z1 = z1
z1 = z2
z2 | z0 | z1 | z2
x1 | 0.6924 | 0.1538 | 0.488
x2 | 0.1538 | 0.6924 | 0.488
x3 | 0.1538 | 0.1538 | 0.024
z2 | z0 | z1 | z2
x1 | 0.1084 | 0.0241 | 0.2647
x2 | 0.0241 | 0.1084 | 0.2647
x3 | 0.8675 | 0.8675 | 0.4706

## Slide 31: Combined Decision
The combined sensor provides substantial improvements in overall system performance
E.g. we observe z1 = z0 and z2 = z0
P(x | z1, z2) = (0.692, 0.154, 0.154)
Hypothesis 1 most likely as expected
However if we observe z1 = z0 and z2 = z1.
P(x | z1, z2) = (0.154, 0.692, 0.154)
Hypothesis 2 has high probability because sensor 1 does detection while sensor 2 does discrimination.
If now we observe no target with sensor 2, having detected target type 1 (or 2) with the first sensor, the posterior is given by (0.488, 0.488, 0.024).
That is there is a target (because we know sensor 1 is much better at target detection than sensor 2), but we still have no idea which of target 1 or 2 it is as sensor 2 did not make a valid detection.

## Slide 32: Combined Decision
If sensor 1 gets no detection, but sensor 2 detects target type 1, then the posterior likelihood is given by (0.108, 0.024, 0.868).
That is we still believe there is no target because sensor 1 is better at providing this information.
Practically, the joint likelihood matrix is never constructed (it is easy to see why here, with n = 3 sensors, and m = 3 possible observations and k = 3 possible outcomes, the dimension of the joint likelihood matrix has k × mn = 27 entries.) Rather, the likelihood matrix is constructed for each sensor and these are only combined when instantiated with an observation.
Storage then reduces to n arrays of dimension k × m, at the cost of a k dimensional vector multiply of the instantiated likelihood functions. This is clearly a major saving in storage and complexity and underlines the importance of the conditional independence assumption to reduction in computational complexity.

## Slide 33: Occupation Sensing
Occupancy Sensing: Determine the number of individuals in a room, zone, building, etc.
  Track both location and movement of occupants.
Necessary information for efficient use of lighting and environmental conditioning, as well as security.

## Slide 34: Problems
Occupancy sensing is typically performed with simple devices: Video cameras, IR motion sensors, optical tripwires, CO2 detectors, etc. Cameras are in general not a good idea.
Problems with sensor use:
  Noisy and/or inaccurate responses.
  Expense.
  Location optimization.
  Generic solutions for unique buildings.
Typically large amounts of data are produced, but only simple analysis is performed.

## Slide 35: Goal
Goals:
  Use cheap sensors in a distributed network.
  Develop new, more sophisticated control algorithms.
  Combine sensor inputs through probabilistic
inference to create more accurate occupancy data.
R. H. Dodier, G. P. Henze, D. K. Tiller and X. Guo, “Building occupancy detection through sensor belief networks,” Energy and Buildings, vol. 38, no. 9, pp. 1033 - 1043, 2006.

## Slide 36: Sensor Belief Network

## Slide 37: Sensor Belief Network

## Slide 38: Sensor Belief Network