## Slide 1: Sensor Data Fusion II
NC 812/ESD 812

## Slide 2: Data Fusion

## Slide 3: Automatic Lighting System
Automatic lighting system is to be implemented that will switch the lights on (if lights are off) when people are present in the area or arrive in the area. Following sensors are used in the system. Each sensor gives a binary decision, e.g. light sensor will give decision whether it is bright outside or not, based on an internal threshold, pressure sensor will give decision whether some passed through the area or not etc. The thresholds cannot be changed. Accuracy of the decision is specified by the values of Pd and Pf.
  light sensor: (Pd = 0.9, Pf = 0.15)
  Pressure sensor on the ground (to detect steps of a person) (Pd = 0.8, Pf =0.1)
  Ambience noise sensor (Pd = 0.98, Pf=0.3)
Design a system that will combine the sensor decisions in such a way that Pd of the resulting system is maximized while Pf is minimized. Use any fusion technique: Decision tree, AND/OR/ML or combination of those.

## Slide 4: Statistical Data Fusion
Techniques such as AND/OR/ML assume that all sensors are equally reliable and combine decisions from each.
What are other techniques that can be used for fusing the sensor decisions and help make a decision?

## Slide 5: Example
Is it dark inside?
Noise levels high?
Anyone coming to the room?
Turn lights on
Turn the lights off

## Slide 6: Naïve Bayesian
Bayesian Classifiers are statistical classifiers
  based on Bayes Theorem
They can predict the probability that a data item is a member of a particular class
Simplest Bayesian Classifier is known as the Naïve Bayesian Classifier
  based on an independence assumption (which is usually incorrect)
  performance is still often comparable to Decision Trees and Neural Network classifiers
  First introduced as a “straw man” against which the performance of more sophisticated classifiers could be compared
    One thing that should be checked when evaluating classifier performance: is it better than Naïve Bayes?

## Slide 7: Bayes Theorem
Let X be the data recorded from experiments (evidence)
Let H be a hypothesis that X belongs to class C
In classification problems we wish to determine the probability that H holds given the observed data X
We seek P(H|X), which is known as the posterior probability of H conditioned on X
  e.g. The probability that X is a kangaroo given that X jumps and is nocturnal

## Slide 8: Bayes Theorem
P(H) is the prior probability
  i.e. the probability that any given data is a kangaroo regardless of it method of locomotion or night time behaviour - i.e. before we know anything about X
Similarly, P(X|H) is the likelihood of X conditioned on H
  i.e. the probability that X is a jumper and is nocturnal given that we know H is a kangaroo
Bayes Theorem:

## Slide 9: Independence
The effect of an attribute value on a given class is independent of the values of other attributes. This assumption is known as class conditional independence
  This makes the calculations involved easier, but makes a simplistic assumption - hence the term “naïve”
In almost all real-life examples, the class conditional independence assumption would break down.

## Slide 10: Decision
Consider each data instance to be an n-dimensional vector of sensor data or decision values (i.e. features):
Given m classes C1,C2, …,Cm, a data instance X is assigned to the class for which it has the greatest posterior probability, conditioned on X, i.e. X is assigned to Ci if and only if

## Slide 11: Weather Data
Outlook | Temperature | Humidity | Windy | Play
Sunny | Hot | High | False | No
Sunny | Hot | High | True | No
Overcast | Hot | High | False | Yes
Rainy | Mild | High | False | Yes
Rainy | Cool | Normal | False | Yes
Rainy | Cool | Normal | True | No
Overcast | Cool | Normal | True | Yes
Sunny | Mild | High | False | No
Sunny | Cool | Normal | False | Yes
Rainy | Mild | Normal | False | Yes
Sunny | Mild | Normal | True | Yes
Overcast | Mild | High | True | Yes
Overcast | Hot | Normal | False | Yes
Rainy | Mild | High | True | No

## Slide 12: Conditional Probabilities
Conditional and apriori probabilities are computed based the available data: P(C1) =9/14 and P(C2) 5/14, where class C1 represents “yes” for the game and C2 respresents “no”.
Outlook and temperature data
P(outlook=sunny¦C1)=2/9 | P(outlook=sunny¦C2)=3/5
P(outlook=overcast¦C1)=4/9 | P(outlook=overcast¦C2)=0
P(outlook=rainy¦C1)=3/9 | P(outlook=rainy¦C2)=2/5
P(temp=hot¦C1)=2/9 | P(temp=hot¦C2)=2/5
P(temp=cool¦C1)=3/9 | P(temp=cool¦C2)=1/5
P(temp=mild¦C1)=4/9 | P(temp=mild¦C2)=2/5

## Slide 13: Conditional Probabilities
For humidity and wind data:
P(humidity=high¦C1)=3/9 | P(humidity=high¦C2)=4/5
P(humidity=normal¦C1)=6/9 | P(humidity=normal¦C2)=1/5
P(windy=true¦C1)=3/9 | P(windy=true¦C2)=3/5
P(windy=false¦C1)=6/9 | P(windy=false¦C2)=2/5

## Slide 14: Decision Rule
Given new set of data, it will be classified based on the following rule (Maximum Likelihood)

## Slide 15: Example
Based on the examples in the table, classify the following datum x:
X=(Out=Sunny, Temp=Cool, Hum=High, Wind=strong). That means: Play or not?
Need to determine P(X|C1) and P(X|C2) and determine the class based on the rule described earlier.
P(X|C1)= P(sunny|C1)P(cool|C1)P(hum=high|C1)P(wind=true|C1)
P(X|C1) = (2/9)(3/9)(3/9)(3/9)=2/243
P(X|C2) = (3/5)(1/5)(4/5)(3/5)=36/625
Is P(X|C1)P(C1) > P(X|C2)P(C2)
P(X|C1)P(C1) = (2/243)*(9/14)=0.0053
P(X|C2)P(C2) = (36/625)*(5/14)=0.0206
The datum X is classified as No Play or class C2.

## Slide 16: Automatic Lighting System
Automatic lighting system is to be implemented that will switch the lights on (if lights are off) when people are present in the area or arrive in the area. Following sensors are used in the system. Each sensor gives a binary decision, e.g. light sensor will give decision whether it is bright outside or not, based on an internal threshold, pressure sensor will give decision whether some passed through the area or not etc. The thresholds cannot be changed. Accuracy of the decision is specified by the values of Pd and Pf.
  light sensor: (Pd = 0.9, Pf = 0.15)
  Pressure sensor on the ground (to detect steps of a person) (Pd = 0.8, Pf =0.1)
  Ambience noise sensor (Pd = 0.98, Pf=0.3)
Design a system that will combine the sensor decisions in such a way that Pd of the resulting system is maximized while Pf is minimized. Use any fusion technique: Decision tree, AND/OR/ML or combination of those.

## Slide 17: Decision Logic
Boolean variables:
  Lights ON or OFF (Decision from the system)
  Dark 1 or 0 (output of the light sensor, indicating the lighting conditions in the room)
  Noise 1 or 0 (output of the noise sensor. If noise levels great than some threshold l, noise =1)
  Steps 1 or 0 (output of pressure sensor. If steps detected, steps = 1)

## Slide 18: Decision Logic
First thing to do is to detect whether anyone is present in the room or not.
Let the Boolean variable be Presence.
Presence = 1, if (Noise=1) OR (Steps = 1)

## Slide 19: Decision Logic
If (Presence =1)
  If(dark = 1)
    Lights = ON
  Else
    Do nothing
Else
  Turn the lights off if on.

## Slide 20: Decision Criteria
The evidence or the data measured include, darkness, Steps and Noise. The data vector X is a 3 tuple (D, S, N). Since each variable is binary, there can be total of 8 possible combinations.
There are three possible outcomes or so-called classes:
C1: Turn the lights ON (conclusion: People are present and it is dark)
C2: Turn the light OFF (conclusion: People are not present)
C3: Do nothing (conclusion: People are present and it is not dark)

## Slide 21: Likelihood
What is the likelihood that N =1 if C1 is true?
P(N=1|C1) = P(Noise levels high|people are present) = 0.98
And so on
P(N=1|C2) = P(Noise levels high|people are not present) = 0.3
P(N=1|C3) = P(Noise levels high|people are present) = 0.98

## Slide 22: Likelihood
What is the likelihood that N =0 if C1 is true?
P(N=0|C1) = P(Noise levels low|people are present) = 0.02
And so on
P(N=0|C2) = P(Noise levels low|people are not present) = 0.7
P(N=0|C3) = P(Noise levels low|people are present) = 0.98

## Slide 23: Likelihood Table
 | Data: Darkness |  | Data: Noise |  | Data: Steps | 
Outcome | D=0 | D=1 | N=0 | N=1 | S=0 | S=1
C1 | 0.1 | 0.9 | 0.02 | 0.98 | 0.2 | 0.8
C2 | NA | NA | 0.7 | 0.3 | 0.9 | 0.1
C3 | 0.85 | 0.15 | 0.02 | 0.98 | 0.2 | 0.8

## Slide 24: Example
Based on the posteriori probabilities in the table, classify the following data x:
X=(D=1, N=0, S=1)
X=(D=1, N=1, S=0)
X=(D=1, N=0, S=0)
X=(D=0, N=0, S=0)
X=(D=0, N=1, S=1)
X=(D=0, N=1, S=0)

## Slide 25: Example
Determine the conditional probabilities. Since no apriori probabilities are identical, i.e. 1/3

## Slide 26: Example
Decision about which class does the data belong to will be made based on likelihood:

## Slide 27: Example 2
For the second data set: X=(D=1, N=1, S=0)